## Slide 1: 802.11a PHY Digital Back-end Design
Sean Huang, Kunmo Kim, Paul Kwon, Josh Sanz, Meng Wei
Notes: Sean opens here with introductions

## Slide 2
Why do OFDM in Chisel?
Several Verilog/VHDL implementations of WiFi exist
But they’re not flexible
  Written to support one standard in particular [1]
  Or wrap several standard specific basebands[2]
And they’re big
  880,000 lines of code[1]
  172,000 lines of code[2]
[1] J. Shi, “OpenOFDM.” https://github.com/jhshi/openofdm, 2017.
[2] phthinh, “IEEE 802.11 OFDM-based transceiver system.” https://github.com/phthinh/OFDM_802_11
Notes: Josh talks about this

## Slide 3
802.11a Transmit Chain

## Slide 4
Convolutional Coding
802.11a Tx Encoder
Puncturing
Interleaver & Modulator
Modulation Ctrl
Ctrl
Data
Fully compatible with 802.11a Specification
  Puncturing matrix can be modified on the fly
  Support programmable convolutional coding matrix

## Slide 5
802.11a Tx Encoder - Convolutional Code (7, 6)

## Slide 6
802.11a Tx – Convolutional Encoder (802.11a Standard)
D
D
D
D
D
D
g0 = 1338
g1 = 1718
Ai
Bi
Vi
802.11a default coding rate = ½
802.11a default constraint length (K) = 7
(n,k,m) = (2,1,6)

## Slide 7
Tail-Biting

## Slide 8
802.11a Tx – Puncturing
Image from [1]

## Slide 9
Tx Modulator

## Slide 10
Raised-Cosine Filter
Direct form FIR architecture
TreeReduce addition to reduce critical path delay

## Slide 11
802.11a Receive Chain

## Slide 12
CFO Correction
802.11a RX CFO Estimation and Correction
Packet Detector
CFO Estimation
Data
Data
Data arrives in CFO Correction block and is rotated by phase error
Data arrives at Packet Detector and packet start/end flags generated
CFO Estimation gets new phase error estimation and updates correction
E. Sourour, H. El-Ghoroury, and D. McNeill, “Frequency offset estimation and correction in the ieee 802.11a wlan,”
in IEEE 60th Vehicular Technology Conference, 2004. VTC2004-Fall. 2004, vol. 7, pp. 4923–4927 Vol. 7, Sept 2004.

## Slide 13
Coarse Offset Estimation
802.11a Short Training Field (STF) has 10 repeating sets of a 16-sample pattern
Every 16 samples the pattern repeats
By averaging the phase difference between all of the corresponding pairs, can extract per-sample phase estimate
CFO Estimation is the last block that uses this field, so this is dropped at this stage
16 samples
16 samples
T0
T1
T2
T3
T4
E. Sourour, H. El-Ghoroury, and D. McNeill, “Frequency offset estimation and correction in the ieee 802.11a wlan,”
in IEEE 60th Vehicular Technology Conference, 2004. VTC2004-Fall. 2004, vol. 7, pp. 4923–4927 Vol. 7, Sept 2004.

## Slide 14
Fine Offset Estimation
802.11a Long Training Field (LTF) has 2 repeating sets of a 64-sample pattern
32 sample Guard Interval between STF and LTF
Every 64 samples the pattern repeats
These samples have the coarse correction applied already, so the long fields are required to get the small residual offset still present after the coarse correction
Equalizer also uses LTF, so this field is passed through
Guard Interval
64 samples
32 samples
T0
T1
E. Sourour, H. El-Ghoroury, and D. McNeill, “Frequency offset estimation and correction in the ieee 802.11a wlan,”
in IEEE 60th Vehicular Technology Conference, 2004. VTC2004-Fall. 2004, vol. 7, pp. 4923–4927 Vol. 7, Sept 2004.

## Slide 15
Offset Correction
Correction is done by CORDIC rotation of input I/Q Vector
Estimation block gives a per-sample phase correction estimate (𝞅0)
Each new sample requires more rotation as phase error accumulates
The next phase correction follows the piecewise function
CORDIC
Phase Correction
REAL
IMAG
REAL
IMAG

## Slide 16
Packet Detector

## Slide 17
FFT (& IFFT)
Single-path delay feedback architecture
  Supports radix-2 and radix-4
  FFT sizes: powers of 2
IFFT reuses FFT architecture
Deserializer
Unscrambler
N
N
SDF Chain
FFT
÷ N
÷ N
Re
Im
Re
Im
Re
Im
Re
Im
FFT block diagram
IFFT block diagram
S. He and M. Torkelson, “A new approach to pipeline FFT processor,” in Proceedings of International Conference on Parallel Processing, pp. 766–770, April 1996.
V. Stojanovic, “Lecture 10: Fast Fourier transform: VLSI architectures,” in 6.973 Communication System Design, 2006. MIT OpenCourseWare.

## Slide 18
Zero-Forcing Equalizer
Completely eliminates ISI
BUT…
Amplifies noise
Reduces overall SNR
Channel Inversion
J. W. M. Bergmans, Linear Equalization. Springer-Science+Business Media, B.V., 1996.

## Slide 19
Rx Demodulator
Optimal soft demapping:
-include logarithmic and exponential functions
-not suitable for hardware implementation
Sub-optimal soft demapping
-low complexity
-negligible soft decoding performance loss

## Slide 20
802.11a Rx Decoder
•Support both Hard & Soft decoding
•802.11a requires only hard decoding
•Two Viterbi decoding algorithms are used
•Normal Viterbi Decoding
•Sliding-Window Viterbi Decoding

## Slide 21
802.11a PPDU Frame Structure

## Slide 22
De-Puncturing

## Slide 23
Maximum Likelihood Sequence Estimator

## Slide 24
Viterbi Decoder Algorithm Flow Chart

## Slide 25
How to determine bit width for PM Register?

## Slide 26
Hard Decoding vs Soft Decoding
Soft Decision = Euclidean distance calculation:
Type = FixedPoint(bitWidth, (bitWidth-3).BP)
Hard Decision = Hamming distance calculation
Type = SInt(2.W)

## Slide 27
ACS computation

## Slide 28
Sliding Window Viterbi Decoder

## Slide 29
The Chisel Difference
Concise code
  8,700 lines of implementation
  8,700 lines of testing
  1-2 orders of magnitude less than the Verilog versions
Agile generators
  Can reconfigure for arbitrary number of subcarriers
  Can reconfigure for arbitrary (convolutional) coding schemes
  And more...
Rapid unit testing!

## Slide 30
Reference
[1] ISO/IEC/IEEE 8802-11:2012
[2] MIT opencourseware 6.973
[3] Deepthi Ancha, Implementation of Tail-Biting Convolutional codes, 2008